Up for sale is a 1983 Mercedes Benz 300D that has been SUPER modified.  The answer to the first question of why are you selling this is because unfortunately, right now with the economy and job market, I need the money more than the car.  My loss is your gain.  This is a long list, and there is a lot of stuff going on here, so please read through and feel free to ask me any questions.  I also have hundreds  of pictures and a camera, so any specific stuff you want to see, let me know.  Also, there is so much stuff to list, that I will try and hit the high points for you.

It has just over 350,000 miles on it.  I have complete maintenance records from 100,000 miles with a 50,000 miles gap right before I owned it.  I have owned this car for several years and have done 99% of the work myself. (I am an ASE certified automotive technician).   I have done a TON of work on this thing, Ill separate it into three categories, SVO upgrades, basic repairs, and other upgrades, performance and whatnot.

SVO/WVO UPGRADE- I can tell you quite definitively that you will not find another car with a system like this on it for sale.  Its a fully set up collection and filtration rig with high quality professional parts and specifically designed for long road trips.  Works great around town, but I wanted this setup for skiing and traveling, hence the high capacity, minimal maintenance.  This is an AWESOME fuel system that I have used in all temperatures, down to below freezing, with on board filtration, and huge capacity.  It has Twin additional SVO coolant heated fuel tanks, a 190gph 10 micron pre-filtration system between them, and timed dash control.  The filtration part is almost fully automated, and is designed to filter while driving with minimal screwing around in the trunk.  I am too impatient to have all kinds of pre-filtration nonsense in my yard, and this system moves all that bother to the trunk of the car, AND does it in cold weather.  The system is super professionally installed and works great.

Here is how it works, you pour oil or pump oil into the 20gal collection tank.  You allow the tank to heat up while driving, you flip a switch on the dash to activate your transfer pump.  The pump will then run for 5 minutes, pre-filtering down to 10 micron.  (there is a trunk mounted restriction gauge to help determine pre-filter changing.)  After 5 minutes, the pump will automatically shut off.  There is a feature to the switch that allows you to shut it off any time, AND the tanks are rigged up with a bypass hose so if the 12gal running tank fills up, it shunts fuel back to the collection tank.  Totally trouble free.  You have approximately two fill ups for the running tank in your collection tank.  The oil in the running tank is then filtered again down to 2 microns through a 90gph filter before going to the engine through the switching valves which ALSO have an adjustable semi automated timing mechanism on them.  The valves have optional timed purge or closed loop burn off, and ALSO have a manual valve allowing you to choose which tank you want to purge to.  The lines are totally heated everywhere.  Gauges for this system include twin supply and return temp gauges on the engine, fuel system restriction gauge for both SVO and diesel, Fuel level gauges for both tanks, and lift pump fuel pressure gauge.  The system gives the car a huge range.

OTHER/PERFORMANCE UPGRADES-  Where to start?  The drive-train is from several different cars combined for highway use.  It consists of, a 1983 617 turbo engine, a 1981 240D 4-speed manual transmission, and a 1985 300SD 2.88 rear end.  The 4-speed behind the turbo engine is something never offered by Mercedes, and makes an amazing difference in power and fun levels.  I also recently installed a new clutch, and a custom master to slave line with a stainless steel flex tube verses the old Mercedes rubber one.  All rubber flex discs are oem, and less than a year old.  All drive train mounts are oem and less than a year old as well.  I installed a 2.88 rear end to jump the top speed about 5-10 mph, and I replaced and rebuilt all seals on the rear end itself.  I had it powder coated an azure blue.  I blocked off the EGR, (this can be undone by the way depending on your local emissions laws, the EGR is still there and works), and the car has a turbo boost gauge and exhaust gas temperature gauge.  Next there is a custom 2 and a half to 3 inch exhaust from the flex pipe back with a resonator that separates into twin tips next to each other.  Sounds GREAT, but not too loud.  People will look at this car coming up the street, but not be annoyed.  I also installed a far superior fuel filter for the diesel only fuel system.  The car has a total of 3 high capacity, easy to change cartridge style fuel filters, all with real time restriction measurement devices.  Fuel quality is not a problem.  This car has 8 additional gauges total.  There is an aftermarket CD player with an aux-in for your multimedia music device.  It has two power ports for your additional electronic stuff.  All this is run off of a dedicated 40 amp relay power system and NOT run off some ancient wire meant for something else.  I had a radar detector and a GPS hooked up pretty much all the time.  I’ve also had a laptop and a cell phone hooked up as well at different times.  I made a lot of modifications to make the car as modern as possible and modern electronic device friendly.  There are a lot more things, but generally I tried to keep the engine mostly stock to retain the amazing reliability and tried to upgrade top speed through gearing and tire size.

BASIC REPAIRS- OK, just for some big ticket items we have a new timing chain, new vacuum pump, new front rotors, new front pads, new front calipers, new rear bearings on both sides, repacked front bearings on both sides, less than a year old CV axles on both sides, less than 2 years old rear springs, heavy duty rear shocks, new clutch and all clutch hardware, new brake master cylinder, new clutch master cylinder, new clutch slave cylinder, recent valve adjustment, alignment last year, new front speakers, new starter, recent glow plugs, ect, ect, so on and so forth.  I’ve got a 2 inch thick folder of repairs and upgrades that can be examined.  Basically, if there is anything that interferes with using this car on a daily basis and driving it long distances, I’ve already dealt with it.  I bought this car to DRIVE it, and that’s what I did.  I repaired and enhanced everything that interfered with that goal.  The car was repainted in the last 10 years with oem colors, and looks sharp.  Dash is nearly crackless and had a carpet to keep it that way.

REALITY CHECK- This is an old car.  It was built when Ronald Reagan was in the second year of his presidency.  The Cold War was alive and well.  The original Return of the Jedi was opening in theaters and we would not see our friend Marty Mcfly and his Delorean in Back to the Future for another 2 years.  I have spent many thousands of dollars on this thing and put hundreds of hours into working on it, far more than I would ever make back in this sale.  It has proven to be a reliable, attractive, fun car for me, but never forget that it is old and has its quirks.  I am completely honest and candid in all my car sales, (most are non profitable labors of love).  I would prefer you know what you are getting into vs BS-ing somebody just to unload the car.

PROBLEMS AND UPCOMING MAINTENANCE-This is a list of what I think the next repairs need to be, and existing issues with the car.  The tach does not work (missing amp), the left rear window does not go down, the left rear door does not lock (missing plunger and some internal hang up, should be an easy fix).  The right rear door does not open (this should also be an easy fix).  No door locks are hooked up to the vacuum system.   There are the standard oil leaks (no burning, and not all that bad).  Tires have about 20% tread life on them left. (three year old firestones, no dry cracks, serviceable for probably another season in a non snow climate).  Going to need new rear pads and one of the calipers is a little sticky on the right rear.  (this should happen in the next couple of months, right now they are squeaking a little).  Sunroof leaks a little during heavy rain. (this ends up in the passenger foot well and is another easy fix that I did not get to).  Cruise control does not work.  AC DID work and was fully charged when I bought the car, but I have not turned it on for 2 years, so now it’s a gamble.  Snubber for the fuel pressure gauge has worn down (I will explain this in person in greater depth, but it means the pressure gauge makes a semi irritating little clicking noise now and then.  I have replacements)  Some vacuum control related weirdness with the climate control, heating and defroster work great.  Problems mostly have to do with cabin direction vent control.  Some other little inconsequential stuff, mostly interior trim things and a few small exterior blemishes.  None of these prevent use of the vehicle and the car is fully ready to drive anywhere.